## Slide 1: Inhalation Anesthesia
Dr Rudra Pratap Pandey

## Slide 2
Inhalation anesthetics are administered, and in large part removed from the body, via the lungs.
Their pharmacokinetic characteristics favour predictable and rapid adjustment of anesthetic depth (advantage) but for delivery, a special apparatus is required (disadvantage).
This apparatus includes a source of oxygen (O2) and a patient breathing circuit that in turn usually includes an endotracheal tube or face mask, a means of eliminating carbon dioxide (CO2), and a gas reservoir or vaporizer.

## Slide 3: Vaporizer
A vaporizer is a device to permit controlled exit of aesthetic vapours (concentration calibrated or measured flow mechanism) in measured concentration. Basically of 4 types
              FO or flow over type
              Wick type
              Inject type
              Bubble through type

## Slide 4: Cylinder & regulators
Oxygen cylinder: 7000L (H type) has approx. 2200 psi pressure which is reduced to 35 -50 psi after passing through regulators, meter and conduits.
Oxygen cylinder has a white neck and is connected to anesthesia machine.
Usually oxygen flow rate of 0.5-2.0 L/min is adequate for various species.

## Slide 5: General Information - 1
CBF and intracranial pressure increases in inhalation anesthesia.
MAC is standard index of measuring potency of inhalation anaesthetics.
MAC is defined as the minimum alveolar concentration of an anaesthetic at 1 atmosphere that produces immobility in 50% of subjects exposed to a supramaximal noxious stimulus (50% of the subjects get anaesthetized whereas, remaining 50% do not get to the desired level).
MAC is not affected by duration of anaesthesia, anticholinergic premedicants, >50mm Hg arterial pressure, gender, hyper or hypokalemia.
MAC increases in hyperthermia or CNS stimulation and decreases due to drugs causing CNS depression.

## Slide 6: General Information - 2
Blood gas partition coefficient also called Ostwald coefficient is the ratio of concentration of one compound in one solvent to the concentration in other solvent in state of equilibrium.
BG partition coefficient of 1.7 means at equilibrium the concentration of gas in blood is 1.7 times more than in alveoli.
The relationship is: Higher partition coefficient – higher lipophilicity – higher potency – higher solubility – more anaesthetic needs to be dissolved – slower onset.
MAC decreases as partition coefficient increases generally.

## Slide 7: Inhalation anesthetic delivery systems
Mapleson breathing systems
Magil system
Breathing circuits should have minimum dead space, low resistance with a reservoir bag (capacity = body weight x 60 ml rounded off)

## Slide 8: Bains co-axial system

## Slide 9: Vaporizer out of circuit - VOC

## Slide 10: Vaporizer in circuit - VIC

## Slide 11: Parts of standard Murphy cuffed ET tube
Tube size in dogs ranges from 1.5 to 15 mm
Brachycephalics need less diameter ET)

## Slide 12: Induction-
General anesthesia can be induced by administering anesthetic gas mix via a facemask or other suitable delivery system connected to ET tube.
Lignocaine spray can be used in dogs but not needed in cats for intubation.
Forcing the ET tube may damage the mucosa and lead to post anaesthetic edema and obstruction.
Laryngeal spasm is common in cats during extubation so tube should be removed when its in proper GA.

## Slide 13: Induction-
There are two methods; ‘incremental’ or ‘crash’ induction.
‘Incremental’ induction technique uses 3 min of preoxygenation and then introduction of 0.5 % vapor setting for 30-60 seconds and then 0.5 % increment for the same period.
‘Crash’ induction is achieved with 3-5 % vapor set of isoflurane following pre-oxygenation.
It is preferable to use non-rebreathing circuits for quicker induction and then switched to the circle rebreathing systems even for animals weighing more than 6 kg.

## Slide 14: Agents -
General anesthesia can be induced by administering via a facemask or other suitable delivery system connected to ET tube.
halothane (having Cl, Br and F),
isoflurane (having Cl and F),
sevoflurane (having only F), or desflurane

## Slide 15: Halothane (halogenated with Br, Cl, F)
1 MAC halothane in dog is 0.8 %.
Vapor setting is at 3-4 % at induction with oxygen flow at 60 ml/kg/min
Vapor setting between 1-3 % during the maintenance with oxygen flow at 20 ml/kg/min.
Halothane is largely being replaced by isoflurane everywhere due to its adverse effect on liver.
As anesthesia is deepened by increasing halothane concentration, CO and arterial pressure decrease further. HR usually remains constant.
Halothane can be used in isoflurane vaporizer and vice versa in emergency as the vapour pressure is almost equal for both.

## Slide 16: Isoflurane (halogenated with Cl & F)
1 MAC in dogs is 1.3%
Isoflurane has replaced halothane both in human and veterinary markets worldwide
Quicker anesthetic stabilization and more rapid recovery than halothane due to its lower blood gas solubility.
Vapor setting is at 3-4 % in dogs at induction with oxygen flow at 60 ml/kg/min and is reduced between 1.5-3 % during the maintenance with oxygen flow at 20 ml/kg/min
Isoflurane, similar to halothane, induces a dose-dependent cardiovascular depression.
Isoflurane causes more peripheral vasodilation than halothane, which is responsible for a low arterial blood pressure, but tissue looks more bright and pink indicating better perfusion.
Isoflurane is less prone to cause arrhythmia compared to halothane

## Slide 17: Sevoflurane (halogenated with F)
Sevoflurane (1 MAC = 2.3 %) is less potent than halothane or isoflurane.
Anesthetic induction, recovery, and intraoperative modulation of anesthetic depths are faster than halothane and isoflurane.
More expensive than halothane and isoflurane.
Sevoflurane induces dose-dependent cardiovascular depression to a degree similar to that of isoflurane.